## Slide 1: ENGI 301 Glucose Sensor Proposal
12/13/2022
Ibrahim Al-Akash

## Slide 2: Background Information
3.7 million people die from diabetes and high blood glucose levels
  422 million diabetics around the world
  1 in 11 people have diabetes
To effectively treat diabetics, patients must monitor glucose levels using current methods:
  Invasive procedures that require implantation of a device
  Painful finger prick tests produce a lot of waste and are not reusable
These methods require patients to actively monitor their glucose, which is inconvenient and reduces patient compliance
Notes: Include something on the right wavelengths on the IR spectroscopy.

## Slide 3: Concept
+
Embedded Sensor System
Sensor Holster
=
Noninvasive Continuous Glucose Sensor
Sensing Mechanism:
NIR Reflectance Spectroscopy

## Slide 4: Concept System
LEDs
Clip bottom view
(surface touching skin)
NIR Sensor
Clip top view
(surface touching garment)
PocketBeagle
Power Source
QI Charger

## Slide 5: System Block Diagram

## Slide 6: Flow Chart
Data Acquisition
1
Data Processing
2
Calibration/Training Regression
3
Classify BGL and Report Values
4
Glucose Dashboard
140mg/dL
Healthy
Notes: Look up software aspects prior to arrival of materials (3 weeks)

## Slide 7: Power Block Diagram
I/O | Voltage | Current
Pocket Beagle | 5V | 140-230 mA
IR Sensor | 3.3V | 100 mA
IR LED | 3.3V | 50 mA
HT16K33 7SEG | 5V | 30mA
LEDs | GPIO | 20mA
Button | 3.3V | 20mA
Notes: MVP

## Slide 8: Roadmap
Basic Hardware (MVP Sensor)
Portability
Wireless Power Capabilities
Bluetooth Interface with PC
Android Bluetooth App
NIR Sensor circuit integrated with PB
Powered by basic USB
Button to start sensing
LEDs to indicate readings
Screen to display numerical data
Powered by USB battery
Powered by LiPo batteries
Include QI coils with charging circuit to recharge LiPo batteries
Initiate sensing and transmit data to PC via Bluetooth
Develop finished smartphone application with interface to initiate sensing and view data
Store data over time
View trends and send notifications highlighting progress

## Slide 9: Components / Budget
Component | Need to Buy | Cost
NIR LED 950nm (Mouser Part #755-SIR-34ST3F) | 1 | $0.87
NIR Sensor (SparkFun Spectral Sensor Breakout) | 1 | $27.95
HT16K33 7-Segment Display | 1 | Included in Class Kit
Red LED | 1 | Included in Class Kit
Yellow LED | 1 | Included in Class Kit
Green LED | 1 | Included in Class Kit
Button | 1 | Included in Class Kit
PocketBeagle | 1 | Included in Class Kit
Total |  | $28.82
Notes: Update links to websites